## Slide 1
Iron Car Final Presentation
Simon Rummert - 27.06.2017

## Slide 2
Goals
Progress
Results
Problems
Future Work
What do we want to talk about?

## Slide 3
Goals
Refactor and update existing Stereo-Vision code
Improve Stereo Vision Quality
Implement Collision Avoidance Algorithm

## Slide 4
Goals
Refactor and update existing Stereo-Vision code
But Why?
OpenCV 3.0.0 Release Date: June 2015
Improvements over OpenCV 2.4.X:
Faster
More stable
Improved usage of multiprocessor and GPU architectures

## Slide 5
Goals

## Slide 6
Goals
Improve Stereo Vision Quality
But Why?
Old cameras supply mediocre depth perception because:
Unsynchronized image capturing
Random frame drops on change of brightness
Only support 320x240 resolution

## Slide 7
Goals
Improve Stereo Vision Quality
But Why?
We want good results even from simple Block Matching Algorithm (It is not so accurate, but faster)

## Slide 8
Goals
Improve Stereo Vision Quality
But Why?
We DO NOT want unsatisfying or noisy results

## Slide 9
Goals

## Slide 10
Goals
Implement Collision Avoidance Algorithm

## Slide 11
Goals
Implement Collision Avoidance Algorithm
But Why?
To avoid collisions...

## Slide 12
Goals

## Slide 13
Progress

## Slide 14
Progress
Update to OpenCV 3.0.0:
Relatively straight forward
Mainly changes in the cmake process
Some function parameters had to be adjusted
Refactoring

## Slide 15
Progress

## Slide 16
Progress
Used new cameras:
Stereo Vision Improvements
Two PS3 Eye Cameras
Cheap
Constant frame rate
640x480 at 30 FPS
Can be hardware synced

## Slide 17
Progress
What is hardware sync?
Stereo Vision Improvements
- Two cameras shoot images at exactly the same time
- Resulting image pair produces better depth perception

## Slide 18
Progress
How does it work?
Stereo Vision Improvements
Left camera:
Cable soldered to VSYNC pin
Right camera:
Cable soldered to FSIN pin

## Slide 19
Progress
How does it work?
Stereo Vision Improvements
VSYNC
sends signal when image is taken
FSIN
receives signal and forces camera to take image

## Slide 20
Progress
Pin locations on the board
Stereo Vision Improvements

## Slide 21
Progress
Next step: Building a Mount
Stereo Vision Improvements

## Slide 22
Progress

## Slide 23
Progress
Idea: Use Tentacles
Collision Avoidance

## Slide 24
Progress
Idea: Use Tentacles
Collision Avoidance
Top View
With Tentacles

## Slide 25
Progress
Idea: Use Tentacles
Collision Avoidance
One Tentacle represents one steering angle
Red means collision imminent
Green means safe
Therefore: always choose green angle
With Tentacles

## Slide 26
Progress
But which safe angle should I choose?
Collision Avoidance
Should I choose left?

## Slide 27
Progress
But which safe angle should I choose?
Collision Avoidance
Should I choose right?

## Slide 28
Progress
Collision Avoidance
Solution: Assume collision object at the side of most intersecting tentacles
Prefering RIGHT side
Prefering LEFT side

## Slide 29
Results

## Slide 30
Results
Remember the goal:
Drive around the obstacles
without collision

## Slide 31
Results

## Slide 32
Results
Why did the car take so long to steer?

## Slide 33
Problems

## Slide 34
Problems
Measurements have shown:
Depth map creation with new cameras: ~500ms per iteration
Depth map creation with old cameras: ~130ms per iteration
Why?
New cameras have 640x480 resolution
That is 2 times the resolution of the old cameras
In total: 4 times more pixels for the depth map calculation

## Slide 35
Problems
Then why bother at all? Just use the old cameras!

## Slide 36
Problems
Results on the same course with old cameras:

## Slide 37
Problems
Then why bother at all? Just use the old cameras!
Remember: We are using the faster, but more inaccurate Block Matching algorithm for our depth map
This means:
  depth map can get too noisy
Therefore:
  Turn down the sensitivity to reduce false positives

## Slide 38
Problems
Then why bother at all? Just use the old cameras!
Depth map with new cameras
Depth map with old cameras

## Slide 39
Problems
Conclusion
New cameras:
Pro:
More accurate depth map
Con:
- Slower calculation time
Old cameras:
Pro:
Overall faster depth map creation
Con:
- Too inaccurate

## Slide 40
Future Work

## Slide 41
Future Work
Use a Multiprocessing/GPU approach for improving the execution time
  Use multiple threads for Image Processing
  Intel‘s TBB library for multiprocessing is used by OpenCV, with workarounds also compilable on Raspberry Pi 2 and 3
  Wait for OpenCL to be implemented for Raspberry

## Slide 42
THE END